## Slide 1: Image Processing Path
Zero.lin

## Slide 2: Chain and function match
Convert to rgb
scale
AHD
Write

## Slide 3: Systematic Sensor Data Correction
Dark Floor Subtraction
  Cause: thermal noise and other nonphoton-generated noise
  Method: subtract a fixed value or a “lens cap” shot
  In Dcraw: support both methods
Structured Noise Reduction
  Cause: sensor is imperfect, defective pixels and variations in the thickness of the CFA color filters
  Method: subtract a dark floor mask
  In Dcraw: delete defective pixels

## Slide 4: CFA Data Correction
Stochastic Noise Reduction
  Method: low-pass filtering, sigma filtering and median filtering
  In Dcraw: wavelet denoise
  Note: if a system consists of a number of operations that are signal amplifiers, then it is best to reduce noise contributions as early as possible in the chain
Exposure and White Balance Correction
  Cause: digital cameras cannot automatically adjusts the apparent exposure and white point
  Method: user specify or automatic exposure and white balance correction
  In Dcraw: specify or average a region pixels

## Slide 5: Adjusted CFA Image and Image Data Calibration
Color Filter Array Interpolation
Stochastic Color Noise Reduction
  Method: low-pass filtering, sigma filtering and median filtering
  In Dcraw: median filtering
  Note: It is far better to transform the image into a luminance-chrominance representation
Color Correction
  Cause: prepare the image for its final rendered form
  Method: transform the image into a standard calibrated color space
  In Dcraw: support {sRGB, Adobe RGB (1998), WideGamut D65, ProPhoto D65, XYZ}

## Slide 6: Image Space Rendering
Tone Scale and Gamma Correction
  Cause: human visual system’s ability to adapt to a wide range of scene luminances
  Method: point transform of the image data
  In Dcraw: support
Edge Enhancement
  Cause: make it look sharper
  Method: direct convolution, unsharp masking
  In Dcraw: no support

## Slide 7: Conclusion
Dcraw has almost the same path as described path, except dcraw consider chromatic aberration the path doesn`t, the path consider edge enhancement which dcraw doesn`t involve.

## Slide 8: Thanks